## Slide 1
Do we really know everything about relay hot switching?
Arlo Blanco

## Slide 3
Doctor’s Appointment
Migraine
or
Brain Tumor

## Slide 4
Device Won’t Pass (DWP)
Site to site issues
After isolation,
You found out it was due to a failing relay
Relay was replaced
The next day, setup is down due to DWP again, but on a different Site
After isolation,
You found out again that it was due to that same kind of relay
Relay was replaced, and setup is fixed
Setup is now passing
Never ending cycle
** Based on 2014 data, an annual total of 720 production hours lost due to DWP issue
1 Month loss
Notes: We can do this again an again..
But we are engineers.. Like the doctor in the previous example
Us, engineers were born to find for root causes and solve the problem
If not, our PDO will be affected.

## Slide 5
$5 each
4 Tester Setups
1 Relay replacement per day
4 Relay replacements per day
Whole year
1460 Relay replacements per year
Cost per year
1460
X $5
$7300
Php 335,800
per year
What if 5 or more setups?
Just one device

## Slide 6
Frequent
Relay
Failure
Total of 32 Affected Relays per loadboard
.. And a lot of different active and passive components
Notes: Board complexity – 32 relays per loadboard
Active and passive components

## Slide 7: Why do we need relays?
A Relay is an electrically operated switch
.. We need to turn things ON & OFF
Mechanical Relay
2
3
4
Off
On
Notes: Explain relay operation
Ideal resistance of a relay = 0ohm
Use numbers
And create separate tables

## Slide 8
For FA
Not Switching
Notes: Possible causes of damage
Typical signature of electrical stress
Voltage used
Toggles
Not end of life
Abused
End of life
Hot switching
Explain effect to testing
Ideal readings table

## Slide 9
Relay stuck-up where contacts were welded to each other
Defective Relay
Good Relay
Notes: Create animation on working and stuck relay
Highlight welding and stuck terminal – show weld

## Slide 10
Man
Machine
Material
Method
Tester issue
Loadboard Design
End of life
Overcurrent
Hot Switching
Wrong Relay
Installed
Fishbone Diagram
Defective Relay

## Slide 11: Probable Causes
Overcurrent
- Current forced on the test program is way above the rated specifications of the relay
Test Program
Relay Datasheet
End of life
- Relay has reached its usable life due to performing its maximum number of toggles
Test Program
Relay Datasheet
Hot Switching
- Turning on a switch where a potential difference is present between the terminals to be connected
Failure is actually too early
Expected = ~10M
Actual = ~600k
Welding is an indicator
of Hot Switching
Notes: Create fishbone prior this slide

## Slide 12: What is Hot Switching?
+V
0V

## Slide 13
+V
0V
+V
+V
Cold Switching
0V
0V

## Slide 14: How to catch hot switching?
Oscilloscope
Loadboard
Schematic
Test Program

## Slide 15
Sample of Good scope reading
Evidence of Hot Switching
+18V
0V
Notes: Explain scope readings
Mention sources - can be supplied or from charged cap

## Slide 16
No Issues found
Test Program Audit
.. Searched for Potential Hot Switching occurrences
Cold switching method was followed
No power supplies left ON before switching
Power up & power down statements are in the correct sequence

## Slide 17: WTF??
Why are we still encountering hot switching???
If it is following the correct procedure..
(Why The Fail?)

## Slide 18: Brainstorming..
Why???
Water Tank
Capacitor
Power Supplies

## Slide 19
Loadboard
Schematic
Capacitors
Affected Relay
Something strange..
Test
Loadboard
Schematic
Capacitors
No Electrical Connection
Looking further...

## Slide 20: More Evaluations..
Open socket test
- Testing without any unit placed
No Hot Switching issues
Confirmed Hot Switching issues
Device Testing
Capacitors
Capacitors
Current Bridge

## Slide 21: Concluded that..
+18V
0V
A lot of times..
Hot Switching
Notes: Looking back at our scope readings – slow discharge – capacitor

## Slide 22: Solution Options..
1) Remove the Capacitor
- needed for testing
2) Add a resistor to discharge the current
- testing failed with the presence of a resistor
3) Use the tester to discharge the current
- This might work!

## Slide 23: Fixing the problem
How do we discharge the capacitor using the tester?
Invulnerable to
hot switching
Solid State Relay
tester channel
Notes: Expound on fix
Options fixing hot switching – choose best option – resistor – remove cap – use different path
Before and after scope shots

## Slide 24
Before
After

## Slide 25: Effect..
95%
reduction in relay replacement
per QTR
Notes: Show relay savings 1st

## Slide 26
Cost Savings
Frequent repairs = multiple downtime
= Capacity loss
Yield loss
Relay replacement
Tech Support for
repairs
What was solved?

## Slide 27: And the best thing about it…
Project is ZERO COST
.. Best things in life are free

## Slide 28: Technical Paper Innovation
Test Program
Information Breakthrough

## Slide 29: Fan-Out / Recommendation
TIPI
TITL TIM TIEM TMX
Chengdu FAB Subcons…
Clark
Training done
QFN Test
Probe
A B C D E F G H I J K L M N O P Q R
Devices with Frequent Relay Replacement Issues
Notes: Animate – focus
Conducted a training at Clark

## Slide 30: Acknowledgment
I would like to thank the following people for support on this project:
For Technical Advice:
Butch Balanon (Apps)
Mike Rigos (PE)
Patrick Callo (PELD)
Noriel Pachejo (PE)
Noel Gregorio (PELD)
For Relay Evaluation support:
Adnel Carbonell (C-shop)
Edison Audar (C-shop)
Engineering Tester Allocation Support:
Philip Cabatbat (VLCT MFG)
Shirlyn Mates (BU Planner)
Millet Paguyo (Cap Planner)

## Slide 31: Always remember…
..Then turn me ON
Turn everything else OFF…

## Slide 32: Thank you!

## Slide 34: Relay Datasheet